Corrigendum in Technical Specification for Tender No. CC-1/2007

Section III: Schedule of Requirement

1(a). Server - Dual Processor based (All the options have to be quoted).

(i) AMD Based (Option – 1)

| Parameters | Original Specification | Revised Specification |
| --- | --- | --- |
| Chipset | Either of the following :- AMD Chipset 8111 & 8132 Broadcom Serverworks HT-2100 Northbridge and HT1000 Southbridge Chipset | Either of the following :- AMD Chipset 8111 & 8132 Broadcom Serverworks HT-2100 Northbridge and HT1000 Southbridge Chipset Nvidia MCP 55 Pro |
| Form Factor (new parameter) |  | Rackmountable |
| Storage | 8 Nos. Hot Plug 146GB 3Gb/sec SAS Disks with 15000 RPM or higher in RAID-5. | 8 Nos. Hot Plug 146GB 3Gb/sec SAS Disks with 10000 RPM or higher in RAID-5. |
| Backup Device | Internal Digital Linear Tape (DLT) Drive with 40/80 GB or higher. | Internal/External Digital Linear Tape (DLT) Drive with 40/80 GB or higher. |
| Server Management Software | Web based monitoring for: - Support Remote Access & Remote monitoring Server trouble shooting Health Indicator and Corrective Action including Auto Mated Power Cycling OS Watch DOG Timer and Fault Resilient Booting Raid Array Diagnostic Tool with ability to view Disc status and array status with pre-failure warning capability. | (i) Web based monitoring for: - Support Remote Access & Remote monitoring Server trouble shooting Health Indicator and Corrective Action including Auto Mated Power Cycling. Raid Array Diagnostic Tool with ability to view Disc status and array status with pre-failure warning capability. (ii) Enhanced Intelligent Platform Management Interface (IPMI) Card |
| Other features, if any | Support Memory Mirroring/Memory Sparring, Hardware Periodic Memory Scrubbing for Enhanced Memory throughput | Parameter Deleted |

1(a)(ii) Intel Based (Option – 2)

| Parameters | Original Specification | Revised Specification |
| --- | --- | --- |
| Processor | 2 x Dual Core Intel Xeon DP CPU 3.6 GHz or higher with 2MB L2 or more cache. | 2 x Dual Core Intel Xeon CPU 3.0 GHz or higher with 4MB L2 or more cache. |
| PCI | Atleast 4 with two hot-plug 64-bit/100/133 Mhz PCI-X and two PCI Express x4/x8 slots. | Atleast 4 with two 64-bit/100/133 Mhz PCI-X and two PCI Express x4/x8 slots. |
| I/O Ports | At least 1 parallel, 1 serial and 4 Nos. USB 2.0(2 in front and 2 in rear), 3 RJ45 Port, 1 PS/2 Keyboard Port, 1 PS/2 Mouse Port. | At least 1 serial and 4 Nos. USB 2.0(2 in front and 2 in rear), 3 RJ45 Port, 1 PS/2 Keyboard Port, 1 PS/2 Mouse Port. |
| Floppy Drive | Internal 3.5” 1.44 MB floppy drive | 3.5” 1.44 MB floppy drive |
| Server Management Software | Web based monitoring for: - Support Remote Access & Remote monitoring Server trouble shooting Health Indicator and Corrective Action including Auto Mated Power Cycling OS Watch DOG Timer and Fault Resilient Booting. Raid Array Diagnostic Tool with ability to view Disc status and array status with pre-failure warning capability. | (i) Web based monitoring for: - Support Remote Access & Remote monitoring Server trouble shooting Health Indicator and Corrective Action including Auto Mated Power Cycling. Raid Array Diagnostic Tool with ability to view Disc status and array status with pre-failure warning capability. (ii) Enhanced Intelligent Platform Management Interface (IPMI) Card |

1(c). Server - Single Processor based (All the options have to be quoted).

(i) AMD Based (Option –1)

| Parameter | Original Specification | Revised Specification |
| --- | --- | --- |
| Chipset | Either of the following :- AMD Chipset 8111 & 8132 Broadcom Serverworks HT-2100 Northbridge and HT1000 Southbridge Chipset | Either of the following :- AMD Chipset 8111 & 8132 Broadcom Serverworks HT-2100 Northbridge and HT1000 Southbridge Chipset Nvidia MCP 55 Pro |
| Form Factor (new parameter) |  | Rackmountable |
| Storage | 6 Nos. Hot Plug 146GB 3Gb/sec SAS Disks with 15000 RPM or higher in RAID-5. | 6 Nos. Hot Plug 146GB 3Gb/sec SAS Disks with 10000 RPM or higher in RAID-5. |
| Backup Device | Internal Digital Linear Tape (DLT) Drive 40/80 GB. | Internal/External Digital Linear Tape (DLT) Drive with 40/80 GB or higher. |
| Server Management Software | Web based monitoring for: - Support Remote Access & Remote monitoring Server trouble shooting Health Indicator and Corrective Action including Auto Mated Power Cycling OS Watch DOG Timer and Fault Resilient Booting Raid Array Diagnostic Tool with ability to view Disc status and array status with pre-failure warning capability. | (i) Web based monitoring for: - Support Remote Access & Remote monitoring Server trouble shooting Health Indicator and Corrective Action including Auto Mated Power Cycling. Raid Array Diagnostic Tool with ability to view Disc status and array status with pre-failure warning capability. (ii) Enhanced Intelligent Platform Management Interface (IPMI) Card |
| Other features, if any | Support Memory Mirroring/Memory Sparring, Hardware Periodic Memory Scrubbing for Enhanced Memory throughput | Parameter Deleted |

(ii) Intel Based – (Option – 2)

| Parameter | Original Specification | Revised Specification |
| --- | --- | --- |
| Processor | Single processor Dual Core Intel Xeon 2218 2.6 GHz or higher with 2MB or more L2 cache. | Single processor Dual Core Intel Xeon 2.66GHz or higher with 4 MB or more L2 cache. |
| FSB | 1066 MHz | 1333MHz |
| Chipset | Intel 3000 | Intel 5000V / 5000P |
| Server Management Software | Web based monitoring for: - Support Remote Access & Remote monitoring Server trouble shooting Health Indicator and Corrective Action including Auto Mated Power Cycling OS Watch DOG Timer and Fault Resilient Booting Raid Array Diagnostic Tool with ability to view Disc status and array status with pre-failure warning capability. | (i) Web based monitoring for: - Support Remote Access & Remote monitoring Server trouble shooting Health Indicator and Corrective Action including Auto Mated Power Cycling. Raid Array Diagnostic Tool with ability to view Disc status and array status with pre-failure warning capability. (ii) Enhanced Intelligent Platform Management Interface (IPMI) Card |

Schedule II : Desktop Computers.

| Parameter | Original Specification | Revised Specification |
| --- | --- | --- |
| Certification | New Parameter | Red Hat Certified |

# Schedule III : Laptops

| Parameters | Specification | Revised Specification |
| --- | --- | --- |
| Memory | DDR2 512MB 667-MHz Two SODIMM slots supporting dual channel memory supporting 512MB/1GB/2GB modules Upgradeable to 4GB or more. | DDR2 512MB 400-MHz or higher Two SODIMM slots supporting dual channel memory supporting 512MB/1GB/2GB modules Upgradeable to 4GB or more. |
| Communication | Integrated 10/100 ethernet. Integrated 56K v.92 Modem Integrated Infrared port compatible with IrDA Standards 1.1 (Fast IR) and 1.0 (Slow IR). | Integrated 10/100 ethernet. Integrated 56K v.92 Modem |
| Certification | New Parameter | Red Hat/SUSE Certified. |

Schedule IV: Thin Clients.

| Parameter | Original Specification | Revised Specification |
| --- | --- | --- |
| Processor | AMD Geode NX 1 GHz or above Fan Less Embedded Processor | Either of these - AMD Geode NX 1 GHz or above Fan Less Embedded Processor VIA C7 1 GHz or above Fan Less Embedded Processor VIA Eden 1 GHz or above Fan Less Embedded Processor |
| Operating System | Embedded Red Hat Enterprise Linux 4 and above. Compressed read-only file system. NFS and Samba file system support. CUPS/LPR/LPD and Samba print support for Deskjet, Laserjet and Dot Matrix printers. X11R6 local Windows manager. Password protected setup. | Embedded Red Hat Enterprise Linux 4 or any other Linux Operating System with kernel 2.6.18 and above. Compressed read-only file system. NFS and Samba file system support. CUPS/LPR/LPD and Samba print support for Deskjet, Laserjet and Dot Matrix printers. X11R6 local Windows manager. Password protected setup. |
| Local Applications | Local Red Hat Enterprise Linux 4 with Open Office 2.0.4 or latest Firefox 1.5.x with Sun JVM 1.5 upwards support Adobe Acrobat Reader (Latest version) Flash Player Local Mail Client Support. | Local Linux OS with Open Office 2.1 or latest Firefox 1.5.x or latest with Sun JVM 1.5 upwards support Adobe Acrobat Reader 7.0 or latest. Flash Player Local Mail Client Support. Support for Devanagari script with Unicode font and available in Remington/ Phonetic/ Transliteration/ Inscript keyboard layouts. |
| Memory | 512 MB SODIMM DDR Memory upgradeable to 1GB or more. | 512 MB DDR/DDR2 Memory upgradeable to 1GB or more. |
| Audio | 1/8-inch mini microphone, Internal Stereo amplified speaker, 1/8-inch mini full 16-bit stereo | 1/8-inch mini microphone, External Stereo amplified speaker, 1/8-inch mini full 16-bit stereo |
| Networking | Integrated 10/100 Mbps auto sensing Ethernet with RJ-45 connector. TCP/IP with DNS and DHCP. Wake on LAN DHCP support for automatic upgrades and unit configuration. PPP | Integrated 10/100 Mbps auto sensing Ethernet with RJ-45 connector. Wireless LAN 802.11 TCP/IP with DNS and DHCP. Wake on LAN DHCP support for automatic upgrades and unit configuration. PPP |
| Security | Password Protection setup. Kensington Lock Support | Password Protection setup. |
| Power Supply | 50 Watts or less power supply. No moving parts in the Thin Client. | 65 Watts or less power supply. No moving parts in the Thin Client. |
| Mounting of Thin Clients | Desktop/Vertical VESA Mounting with kit. | Desktop/Vertical VESA Mounting with kit.. The Thin Client can be mounted on the TFT with substantial stability. |
| Regulatory Standards | Regulatory standards FCC, UL and RoHS compliant. | Parameter Deleted |
| Management Tool (to be supplied as part of Thin Client Management Software) | Thin Client Management software tool complaint with HTTP/HTTPS/SNMP with following features: - Single Deployment; Secure Management; Remote management, configuration and upgrades through management software; Complete image upgrade; Send messages; Easy migration; Wake Client Remotely (Wake on LAN) Remote Screen Shadowing of entire desktop (via VNC viewer); PXE BIOS for image network boot. | Thin Client Management software tool complaint with HTTP/HTTPS/SNMP with following features: - Single Deployment; Secure Management; Remote management, configuration and upgrades through management software; Complete image upgrade; Send messages; Easy migration; Wake Client Remotely (Wake on LAN) Remote Screen Shadowing of entire desktop (via VNC viewer); PXE BIOS for image network boot. Software should be Linux based. |

Schedule V : Laser Printers.

5(b). Laser Printers

| Parameter | Original Specification | Revised Specification |
| --- | --- | --- |
| Print Speed | 20 ppm | 22 ppm |
| Warranty | Three Years Comprehensive on-site warranty. | Three Years Comprehensive on-site warranty from OEM. |

## Schedule VI : Line Matrix Printers

| Parameter | Original Specification | Revised Specification |
| --- | --- | --- |
| Print Speed | Print Speed (LPM, upper case characters, lower case characters) :- High Speed – 1200/1028 Graphics Speed :- 60 x 72 dpi – 100 inches per minute | Print Speed (LPM, upper case characters, lower case characters) :- High Speed/Draft – 1200/1028 Graphics Speed :- 60 x 72 dpi – 100 inches per minute |
| Typefaces | High Speed, Data Processing, Near Letter Quality | High Speed/Draft, Data Processing, Near Letter Quality |
| Character Pitch | 10,12,13.3,15,17.1,20 | 10,12,13.3 or 13.33,15,17.1 or 17.14,20 |
| Line Spacing | 6,8,10.3,n/72,n/216 | 6,8,10 or 10.3,n/72,n/216 |
| Printable Width | 2.5” to 18.9” | 2.5” to 13.6” or better |
| Emulations | Serial matrix printer, Epson FX 1800, IBM ProPrinter III XL, Printronix P Series, Printronix P Series XQ, DEC LG, ANSI 3.64 | Epson FX 1800 or Epson FX 1180, IBM ProPrinter III XL, Printronix P Series, DEC LG, ANSI 3.64 or Tally ANSI or Genicom ANSI |
| Resident Character Sets | Unicode UTF-8, IBM World Trade, ECMA Latin-1, DEC Multinational, IBM Code Page 437 and 850, OCR A, OCR B | Unicode UTF-8 or Dev Unicode, ECMA Latin-1 or Latin1 8859-1, DEC Multinational, IBM Code Page 437 and 850 or Code Page 437 and 850 |
| Fonts | High Speed, Data Processing, Serif, Sans Serif, OCR-A, OCR-B | High Speed or Draft, Data Processing, OCR-A, OCR-B |
| Bar Codes | Code 39, Code 128, interleaved 2/5, UPC-A,UPC-E, EAN 8, EAN 13, EAN 128, Codabar, Identicon 2 to 5, MSI, POSTNET, Royal Mail, PDF 417 | Code 39, Code 128, interleaved 2/5, UPC-A,UPC-E, EAN 8, EAN 13, EAN 128, Codabar, Identicon 2 to 5, MSI, POSTNET, PDF 417 |
| Paper Handling | Type | Fan folded, Continuous, Edge-perforation | Type | Fan folded, Continuous, Edge-perforation |
|  | Width | 3” to 17” | Width | 3” to 17” |
|  | Copies | Upto 6 parts | Copies | Upto 6 parts |
|  | Thickness | 0.025” | Thickness | 0.025” |
|  | Paper Path | Straight through paper path with easy-load dual adjustable tractors | Paper Path | Straight through paper path with easy-load dual adjustable tractors |
|  | Feed | Bottom feed | Feed | Bottom feed |
|  | Forms Control | 14 and 12 channel electronic vertical format unit, paper-out detector and alarm, paper motion detector and alarm. | Forms Control | 14 and 12 channel electronic vertical format unit or VFU and VT Channel, paper-out detector and alarm, paper motion detector and alarm. |
| Interface | IEEE-1284 Parallel Port, RS-232, Ethernet 10/100 and Wireless 802.11b/g. | IEEE-1284 Parallel Port, RS-232, Ethernet 10/100 |